## Slide 1: ENGI 301 Wearable Metronome Proposal
10/15/2019
Hoang Vu

## Slide 2: Background Information
A wearable metronome/sound sensor, functions include:
  Vibrates at a set tempo
  LED patterns according to noise level
  Optional (different mode for different rhythms/scales)
Advantage: replace traditional sound metronome with vibrational indication direct to musicians
  Do not interfere with recording
  Usable in loud noise situation

## Slide 3: System Block Diagram
PocketBeagle
LED + 680 Ohms resistor
Power Bank
Vibrational Motor
4-digit 7-segment Display
USB Port
I2C2
PWM0BPWM1A
PWM2B
GPIO58
Multifunctional Button
3.3V
GND
GPIO117
330 Ohms Resistor
USB1
Microphone
(through microusb breakout board and audio adapter

## Slide 4: Power Block Diagram
5V
3.3V
85 mA
PocketBeagle
LED + 680 Ohms resistor
Power Bank
Vibrational Motor
4-digit 7-segment Display
USB Port
I2C2
PWM0BPWM1A
PWM2B
GPIO58
Multifunctional Button
GND
GPIO117
330 Ohms Resistor
USB1
Microphone
(through microusb breakout board and audio adapter
3.3V
3.3V

## Slide 5: Fritzing Diagram

## Slide 6: Components / Budget
Component | Need to Buy | Cost
PocketBeagle | No | $22.56
Small vibrational motors | No | $7.99/5
Microroller switch | No | $0.10
LED | Yes | $0.10
4-digit 7-segment LCD Display I2C Adafruit | No | $19.95
Microphone USB Clip-on | Yes | -
10,000 mA power bank | Yes | -
Universal Sport Armband | No | -